## Slide 1
Asynchronous FIFO CDC Design
SystemVerilog/UVM verification study with farm-backed evidence
Post_M5/UVM
canonical target
0
UVM errors/fatals
100%
coverage goals hit
Questa
farm-verified
Asynchronous FIFO CDC Design and Verification Study | 01

## Slide 2
Problem Statement
Safe data transfer across unrelated write and read clocks
Asynchronous FIFO CDC Design and Verification Study | 02
Write domain 80 MHz 12.5 ns
Async FIFO 64 entries 8-bit data
Read domain 50 MHz 20 ns
Preserve FIFO ordering while the two clocks advance independently.
Prevent overflow writes and underflow reads without sharing unsafe dual-clock state.
Generate full, empty, half-full, and half-empty flags with threshold-accurate timing.
Capture proof in simulator transcripts and reviewable waveform artifacts.

## Slide 3
Design Objectives
Implementation and verification goals
Asynchronous FIFO CDC Design and Verification Study | 03
CDC correctness
Synchronize pointers safely across unrelated domains.
Data integrity
Maintain ordering through wraparound, backpressure, and resets.
Flag accuracy
Assert full, empty, half-full, and half-empty at the intended edges.
Evidence quality
Commit farm transcripts, coverage reports, and readable waveform images.
Primary implementation principle
Use local binary pointers for arithmetic.
Send only Gray-coded pointers across clock boundaries.
Place both synchronizer flops in the destination domain.
Compute occupancy locally from the next pointer and synchronized remote pointer.
Verification principle
Drive before the DUT sampling edge.
Monitor accepted transfers, not raw attempts.
Check data with an independent queue reference model.
Use directed tests for exact flag thresholds.

## Slide 4
DUT Architecture
Five-block async FIFO structure
Asynchronous FIFO CDC Design and Verification Study | 04
write_pointer binary -> Gray wFull, wHalfFull
sync_w2r 2 flops in rclk
read_pointer binary -> Gray rEmpty, rHalfEmpty
fifo_memory 64 x 8 storage
sync_r2w 2 flops in wclk
Memory access is gated by local full/empty protection.
Pointer width is one bit wider than the RAM address.
Gray-coded pointers are the only cross-domain state.
Each flag is registered in the domain that consumes it.

## Slide 5
CDC Design Decisions
Why the final RTL avoids common async FIFO traps
Asynchronous FIFO CDC Design and Verification Study | 05
Binary locally
Increment, address, and occupancy math remain simple within one clock domain.
Gray across domains
Only one pointer bit changes per increment before synchronization.
Extra MSB
Same address can mean empty or full depending on pointer wrap state.
Rejected pattern
single fifo_count written by wclk and rclk
Final pattern
next local pointer minus synced remote pointer
Result
CDC-safe occupancy per consuming domain

## Slide 6
Flag Timing Innovation
Write-side half-full and full proof
Asynchronous FIFO CDC Design and Verification Study | 06
Half-full uses `binary_wptr_next`, not the prior registered pointer.
`wHalfFull` asserts when the accepted write reaches 32 entries.
`wFull` asserts when the accepted write reaches 64 entries.
The waveform is generated from the directed farm VCD.
32
half-full threshold
64
full threshold

## Slide 7
Read-Side Flag Evidence
Half-empty and empty threshold proof
Asynchronous FIFO CDC Design and Verification Study | 07
Half-empty uses `binary_rptr_next` for same-edge threshold behavior.
`rHalfEmpty` asserts when occupancy drops to 32 entries.
`rEmpty` asserts when the final accepted read drains the FIFO.
Overflow and underflow attempts are tested without corrupting the scoreboard model.
32
half-empty threshold
0
empty occupancy

## Slide 8
UVM Verification Architecture
Independent agents for independent clock domains
Asynchronous FIFO CDC Design and Verification Study | 08
fifo_random_test or fifo_base_test
fifo_env
write_agent sequencer + driver + monitor
read_agent sequencer + driver + monitor
fifo_scoreboard queue reference model
Separate read and write paths reflect the real CDC split.
Drivers produce stable stimulus before the active edge.
Monitors publish only accepted transfers.
The scoreboard checks ordering independently of DUT internals.

## Slide 9
Scoreboard And Monitor Strategy
Accepted-transfer modeling with reset-aware checking
Asynchronous FIFO CDC Design and Verification Study | 09
Write monitor winc && !wFull
Expected queue push wData
Read monitor rinc && !rEmpty
Compare rData pop expected
Reset monitor flush queue
Aligned model after reset
Farm scoreboard summary
Metric | Result
Writes observed | 659
Reads observed | 596
Reset flushes | 2
Residual queue | 0
Mismatches / errors | 0
Verdict | PASSED

## Slide 10
Coverage Plan
DUT-scoped code coverage plus functional covergroups
Asynchronous FIFO CDC Design and Verification Study | 10
DUT-focused coverage avoids inflating results with testbench code.
Code coverage: statements, branches, expressions, conditions.
Functional coverage: flags, data patterns, reset, bursts, idle cycles, throughput.
Final result: 100% DUT-filtered code coverage and 100% covergroup coverage.
100%
DUT coverage
9
covergroups

## Slide 11
Bug Injection And Robustness
Negative testing confirms the checker can fail for real defects
Asynchronous FIFO CDC Design and Verification Study | 11
Macro | Injected defect | Verification purpose
WDATA_CORRUPTION_BUG | Corrupt write data | Scoreboard catches data mismatch
SYNC_BUG | Remove second sync flop | Exercise CDC assumptions
RPTR_BUG | Use binary read pointer | Test Gray encoding checks
WPTR_FULLFLAG_BUG | Naive full equality | Validate wrap-aware full logic
Default build keeps all defect macros disabled.
Each macro is intended to be enabled independently.
The goal is not only to pass the nominal design, but to prove that meaningful bugs are detectable.

## Slide 12
Final Results And Review Path
Concise evidence for project evaluation
Asynchronous FIFO CDC Design and Verification Study | 12
0
UVM warnings/errors/fatals
100%
DUT-focused coverage
100%
covergroup coverage
PASS
directed flag thresholds
Recommended review path
Post_M5/UVM/async_fifo.sv
Post_M5/UVM/async_fifo_scoreboard.sv
Post_M5/UVM/async_fifo_coverage.sv
Post_M5/UVM/MANIFEST.txt
Closing summary
CDC-safe FIFO RTL with Gray-coded pointer synchronization.
UVM environment with independent agents and reset-aware checking.
Directed waveform evidence for threshold-accurate flags.
Farm-backed transcripts and coverage artifacts committed with the repo.